## Slide 1
2019. 7. 8
Development of Room Occupancy Detection Device
For Smart-FM
*YooSeok, Jung; TaeWook Kang
*yooseok@kict.re.kr
I3CDE Penang
Notes: Hello, this is 정유석 from KICT Korea.
Let me tell you about room occupancy detection, which I have been interested in.

## Slide 2
1. Background
Contents
2. Framework
3. IoT Device installation
1
4. Data collection
5. Deep Learning condition
6. Deep Learning Result
7. Conclusion
Notes: In this research, IoT device is fabricated and collect the data. Than analyzed using Deep learning.

## Slide 3
1. Background
The way and meaning of the office is changed
Shared offices and open offices become common
Furthermore, flexible working is introduced
How to maintain office space must be changed
[ Shared and Open office ]
[ Flexible working ]

## Slide 4
1. Background
Notes: So, new type of office management should be introduce.
Instead of User occupy the space and self-managing, the sensors are collecting the indoor condition automatically and give an information to Facility manager.
Than facility manager is able to manage the office easily.

## Slide 5
2. FrameWork
Gateway
NodeMCU
Temperature
Humidity
Brightness
Room occupancy
Internet of Things
WiFi
Cloud
Big Data
Deep Learning
Deep learning for time-series data
Multi layer perceptron
LSTM (Long short-term memory)
Notes: This research propose the framework as shown.
Space conditions are collected using IoT device.
Than it become a Bigdata on the Cloud.
Deep learning can be adopted to the bigdata.
If a large difference is found, between the actual data and the predicted data using deep learning, there may be an issue in the space.

## Slide 6
3. IoT Device installation
Notes: IoT devices are fabricated using NodeMCU.

## Slide 7
3. IoT Device installation
<DHT.h>, <ESP8266WiFi.h>, <WiFiClient.h>, <ThingSpeak.h>, <Wire.h>, <Adafruit_GFX.h>, <Adafruit_SSD1306.h>
Define libraries
Data aquisition
Connect WiFi
i=20
Data storage
i=0
i=0
i+1
i=0
Temperature, Humidity, Brightness (1s/s)
Send the data to cloud service (+10sec)
Notes: Open source libraries are mainly used.
Temperature, humidity, and brightness data are collected every second.
After 20 data were collected, statistical processing was performed to transmit them to the cloud.

## Slide 8
3. IoT Device installation
Notes: 3 IoT devices are installed at underground floor of KICT.

## Slide 9
3. IoT Device installation
[ Device 1 ]
[ Device 2 ]
[ Device 3 ]

## Slide 10
3. IoT Device installation
Notes: Data in collected using Thingspeak which is IoT platform.

## Slide 11
4. Data Collection
Notes: Due to the air-conditioning system, Temperature and Humidity is not change much.
The brightness show more data change and patterned.
So, brightness data is analyzed first.

## Slide 12
5. Learning condition
Environment : Google Colab(Keras)
Model : Multi Layer Perceptron
Condition : 3-Dense Layer(128neuron) + Output layer(1neuron)
Activation : relu
Data set : 55277 = 40000(train set) and validation set
4 input features(Hour, Minute, Second, Brightness)
epochs=50, batch_size=256
Notes: Learning Condition.
I used Keras at google colab environment.
Multi layer perceptron model is adopted.
More than 50-thousand of brightness data is using for learning and validation.

## Slide 13
6. Learning results
[1 min prediction] Train Score: 780.47, Test Score: 1090.23, MAPE: 2.40
[5 min prediction] Train Score: 4606.68, Test Score: 5966.68, MAPE: 8.23
Notes: Here are learning results.
I increases the prediction time from 1-minute to 25minute.
As you can see, the MAPE(error) is increases the longer the prediction time.

## Slide 14
6. Learning results
[10 min prediction] Train Score: 3893.21, Test Score: 6977.88, MAPE: 10.47
[15 min prediction] Train Score: 6623.33, Test Score: 10181.30, MAPE: 13.73

## Slide 15
6. Learning results
[20 min prediction] Train Score: 7536.59, Test Score: 12577.71, MAPE: 16.30
[25 min prediction] Train Score: 7903.24, Test Score: 15129.51, MAPE: 18.89

## Slide 16
6. Results
Notes: The MAPE is linearly increased.
So If we try to predict lower than the 10 minute of brightness , acceptable Error is occurs.

## Slide 17
7. Conclusion
Verified the possibilities of an office maintenance framework utilizing IoT and deep learning.
10% of MAPE is occurs when the brightness after 10 minutes is predicted
MAPE(error) is increased the longer prediction time.
Further research plan :
  Optimized the input features
  Adopt the LSTM model
  Analyze the other data(Temperature, Humidity, Device #2 and #3)

## Slide 18
Thank you

## Slide 19
2. Background
Indoor space information
- Temperature
- Humidity
- Brightness
Facility Manager
User
-Reserve
-Use
-Analyze
-Manage
Feedback